## Slide 1: CENTEC PTN Solution Introduction
Chen Yuqiang
2018-01-02

## Slide 2: Agenda
接入技术方案
方案介绍

## Slide 3: 硬件形态
PTN交换核960G
千兆接口卡
百兆接口卡
TDM接口卡
万兆接口卡
万兆接口卡

## Slide 4: 接入方案
百兆接口卡和千兆接口卡使用CTC5160芯片，120G交换容量，支持全面的PTN功能和L3功能；
万兆接口卡使用CTC8096芯片，960G交换容量，支持全面的PTN功能和L3功能；
TDM接口卡，支持STM-1和STM-4两种接口，上联通过以太10G口接入到PTN核心交换板；

## Slide 5: 接入方案
接入方案1，PC双上联层二以太接入
  PC端支持静态Linkagg
  千兆/百兆接口卡二层VLAN接入
  起IGMP-Snooping
  起MLAG
  二层方案是否可行看网关需求
接入方案2，PC双上联层三以太接入
  接口卡起三层口，配置成PC网关

## Slide 6: Protection
Ring Protection
  draft-cheng-mpls-tp-shared-ring-protection
  Section OAM Based
  <50ms
Node D
Node A
Node B
Node C
Working LSP
Protection LSP

## Slide 7: End to End Qos
Ingress
  EVC is mapped from port or/port + VLAN.
  Support bandwidth control (CIR, PIR) per flow in Service-policy.
  Support bandwidth control (CIR, PIR) per UNI or EVC.

## Slide 8: Metro Ethernet
Metro Ethernet
  G.8031
  G.8032V1
  Y.1731 & 802.1ag
  EFM
PTN Interwork with Metro Ethernet
  STP on VPLS AC
  G.8032 on VPLS AC
  G.8031 on VPWS/VPLS AC
  G.8032 Dual-home to VPLS(draft-boutros-l2vpn-mpls-tp-mac-wd-00)

## Slide 9: Integrated Network Topology
CE-A
PE-A
PE-B
PE-C
CE-G
CE-D
G.8032 or xSTP
CE-F
CE-B
G.8032 or xSTP
CE-C
CE-E
xSTP on AC
  Link Down/up Trigger
  < 1s Protection
G.8032 on AC
  CFM OAM Based
  <50ms Protection

## Slide 10: Integrated Network Topology
CE-A
PE-A
PE-B
PE-C
CE-C
CE-B
RPL
G.8032 open ring
B
  G.8032 Dual-home with Open Ring
  CFM OAM Based
  MAC Address Withdrawal over Static Pseudowire (draft-boutros-l2vpn-mpls-tp-mac-wd-00)

## Slide 11: Integrated Network Topology
PE-A
PE-B
PE-C
CE-C
CE-B
LinkAGG
G.8031 on AC
  CFM OAM Based
  G.8031 on VPLS AC(<50ms Protection)
  G.8031 on VPWS AC(<50ms Protection)
LinkAgg on AC
  < 1s Protection
CE-A
G.8031

## Slide 12: End
THANKS