## Slide 1: CENTEC PTN Solution Introduction
Chen Yuqiang
2017-07-10

## Slide 2: Agenda
PTN 历史回顾
PTN 基础技术
PTN 现状
盛科PTN历程
盛科PTN案例
盛科PTN方案介绍

## Slide 3: PTN历史回顾
提出
  2008年PTN技术提出，用于替代先前的T-MPLS技术
  2009年中国移动率先宣布选用PTN技术作为下一代承载方案，替代SDH/MSTP，甚至OTN
  2011年MPLS-TP G.8113.1标准确定标志着PTN技术落地
发展
  2009年之后，中国移动组织了多轮PTN测试
  2012年之后，随着3G的大规模部署，PTN迎来了运营商大规模集采阶段
  2013~2014年电信联通确定了类似PTN的IPRAN方案
成熟
  2011~2012年中国移动发布了《PTN技术总体技术规范》标志着PTN技术的稳定和成熟，2013年发布了《集客PTN技术标准》
  目前PTN在中国，日本，韩国，欧洲有着大规模的部署
  厂家主要有华为，中兴，烽火，上贝等

## Slide 4: PTN 典型组网
  PTN典型回传网络组网

## Slide 5: Agenda
PTN 历史回顾
PTN 基础技术
PTN 现状
盛科PTN历程
盛科PTN案例
盛科PTN方案介绍

## Slide 6: PTN 基础技术
  Packet Transport Based
  MPLS-TP
  OAM
  Protection
  Time Synchronization
  End-to-End Qos
  …

## Slide 7: Agenda
PTN 历史回顾
PTN 基础技术
PTN 现状
盛科PTN历程
盛科PTN案例
盛科PTN方案介绍

## Slide 8: PTN现状
技术现状
  PTN承载技术本身趋于稳定，大量的运营商部署验证了技术
  在接入测PTN向着小型化大容量方向发展
  在核心侧PTN向着和OTN融合的方向发展，提出了POTN
  另外目前移动在技术方向上向S-PTN方向上引导
    S-PTN为PTN与SDN结合的技术，移动2015年发布了技术白皮书
    2016年完成了第一次S-PTN互通集采测试
  运营商和设备商都在研究5G承载的PTN技术

## Slide 9: Agenda
PTN 历史回顾
PTN 基础技术
PTN 现状
盛科PTN历程
盛科PTN案例
盛科PTN方案介绍

## Slide 10: 盛科PTN历程
2012年完成基于Humber芯片的PTN方案设计以及海外客户的小规模部署
2013年推出基于Greatbelt芯片PTN/IPRAN方案，凭借完善的OAM方案，赢得大客户的信任
2014~2015年国内PTN/IPRAN客户开始规模部署

## Slide 11: Agenda
PTN 历史回顾
PTN 基础技术
PTN 现状
盛科PTN历程
盛科PTN案例
盛科PTN方案介绍

## Slide 12: 盛科PTN案例
移动回传案例
  双主控，双电源，双风扇
  MPLS-TP,OAM,1588&SyncE，MEF

## Slide 13: Agenda
PTN 历史回顾
PTN 基础技术
PTN 现状
盛科PTN历程
盛科PTN案例
盛科PTN方案介绍

## Slide 14: OAM
MPLS-TP OAM G8113.1
  2k 3.3ms sessions
  CCM,LB,LT,RDI,AIS,LCK,CSF,DM
Service Type
  Section OAM
  LSP OAM
  PW OAM(SS-PW, MS-PW)
PE-A
P
PE-B
Section-OAM
Section-OAM
LSP-OAM
PW-OAM

## Slide 15: Service Support
Service Model
  ELine(VPWS)
  ELAN(VPLS/H-VPLS)
  ETREE(VPLS Based)
  MEF9/MEF14 Pass
Carrier type
  IP(ARP or Static)
  Non-IP

## Slide 16: Protection
Trail Protection (2 level APS)
  G.8131.1
  LSP protection(<50ms)
  PW protection(<50ms)
SNC Protection
  G.8131.1
  SPME(<50ms)
SPME
Working path
Protection path

## Slide 17: Protection
Ring Protection
  draft-cheng-mpls-tp-shared-ring-protection
  Section OAM Based
  <50ms
Node D
Node A
Node B
Node C
Working LSP
Protection LSP

## Slide 18: Clock Synchronization
Clock Synchronization
  1588v2 + G.8264(SSM)
  1588 reference clock from SyncE
  OC, BC, TC(end-to-end and peer-to-peer )
  1PPS + TOD output

## Slide 19: End to End Qos
Ingress
  EVC is mapped from port or/port + VLAN.
  Support bandwidth control (CIR, PIR) per flow in Service-policy.
  Support bandwidth control (CIR, PIR) per UNI or EVC.

## Slide 20: Metro Ethernet
Metro Ethernet
  G.8031
  G.8032V1
  Y.1731 & 802.1ag
  EFM
PTN Interwork with Metro Ethernet
  STP on VPLS AC
  G.8032 on VPLS AC
  G.8031 on VPWS/VPLS AC
  G.8032 Dual-home to VPLS(draft-boutros-l2vpn-mpls-tp-mac-wd-00)

## Slide 21: Integrated Network Topology
CE-A
PE-A
PE-B
PE-C
CE-G
CE-D
G.8032 or xSTP
CE-F
CE-B
G.8032 or xSTP
CE-C
CE-E
xSTP on AC
  Link Down/up Trigger
  < 1s Protection
G.8032 on AC
  CFM OAM Based
  <50ms Protection

## Slide 22: Integrated Network Topology
CE-A
PE-A
PE-B
PE-C
CE-C
CE-B
RPL
G.8032 open ring
B
  G.8032 Dual-home with Open Ring
  CFM OAM Based
  MAC Address Withdrawal over Static Pseudowire (draft-boutros-l2vpn-mpls-tp-mac-wd-00)

## Slide 23: Integrated Network Topology
PE-A
PE-B
PE-C
CE-C
CE-B
LinkAGG
G.8031 on AC
  CFM OAM Based
  G.8031 on VPLS AC(<50ms Protection)
  G.8031 on VPWS AC(<50ms Protection)
LinkAgg on AC
  < 1s Protection
CE-A
G.8031

## Slide 24: Capability
Flexible Capability
  ODUT1# show stm prefer ptn
  ptn profile:
  number of vlan instance : 4094
  number of vlan member ports : 16384
  number of vpls instance : 256
  number of vpws instance : 2048
  number of unicast ipv4 host routes : 512
  number of unicast ipv4 indirect routes : 4096
  number of igmp groups & mcast ipv4 routes : 1024
  number of mac based vlan class : 256
  number of qinq & vlan translation : 2048
  (shared with vpls ac/vpls peer/vpws/allowed vlan on ac)
  number of unicast & multicast mac addresses : 8192
  number of ipv4 source guard : 64
  number of ipv4 based vlan class : 64
  number of mac/ipv4/mpls qos policy rules : 1024
  number of mpls : 8192
  number of lsp : 4080
  number of pw : 4096
  number of flex ac entries : 160
  number of default mpls static block : 64
  number of CFM local&remote MEPs : 4096
  number of G8031 groups : 16
  number of G8032 rings : 16
  number of G8032 member ports : 32
  number of mpls-tp oam session : 2047
  number of link aggregation (static & lacp) : 63

## Slide 25: End
THANKS